## Slide 1: 1. Why soil behaves as it does
Mike Jefferies, PEng
Dr. Dawn Shuttle, PEng
January, 2015

## Slide 2: Preamble
Soil behaves according to effective stress
Drained loadings are vastly quicker with sands
    Explore the nature of soil behaviour primarily using sands
Effect of void ratio initially done using clays as easy to measure void ratio using water content
Modern understanding blends understanding from sands and clays together
    Grain size does not matter
    Everything is particulate
    Accurate ‘as-tested’ void ratio in sands now achievable

## Slide 3: Testing of soils 100 years ago
tvh
sv
Controlling drainage…
  Difficult to encase sample in membrane
  => difficult to measure pore pressure
Only measure half the stresses…
  In plane-strain 4 stresses: sv, sh, tvh, s2

## Slide 4: Triaxial compression test: ~1940 onwards
Measure
  Axial load
  Axial deformation
  Radial stress sr′
  Pore pressure
  Volume change
Compute
  sa′
  ea
  ev

## Slide 5
GDSLab software for hardware control & data acquisition
Serial pad for data acquisition
USB digital pressure controllers for application of confining and back pressures
50 kN USB load frame for specimen shearing
Triaxial cell with internal load cell, pore pressure and axial displacement transducers
Modern simple triaxial equipment
Notes: Primary components of a TAS.

## Slide 6: Advantages and disadvantages of triaxial
Everything is measured
Symmetry and fixed loading-deformation directions
  Gives simplicity, but cannot explore all behaviour
  Not plane-strain
Samples do not deform uniformly
  Need ‘area’ corrections to convert load to stress
  Can do ‘local strain’ measurements
3000 pts to 15% ea

## Slide 7
Triaxial is not ‘perfect’ s-e data…
saxial = F / A
Notes: Visually shows a CD (consolidated drained) triaxial test taking place. Intends to give potential users a feel of what real triaxial test data looks like, along with real specimen deformation.

## Slide 8: Deformation components
=
Deformation = volume change + pure distortion
+
Volumetric strain: ev Deviatoric strain: eq = e1- ev/3
Mean stress: Deviator stress:
p = (sa+ 2sr)/3 q = (sa- sr)

## Slide 9: Drained triaxial test
Controlled by your choice

## Slide 10: Undrained triaxial tests
u
ue
‘stress-path’
Your choice by closing drainage valve

## Slide 11: PRINCIPLE
Soil properties cannot be changed by closing a valve !
Everything fits within an effective stress framework

## Slide 12: Shear box data (Skepton & Bishop, 1950)
Terzaghi model of soil strength

## Slide 13: Example of particle shapes

## Slide 14: 1885: Distortion causes dilation
Reynolds, 1885

## Slide 15: Taylor – Bishop (1950)
Work being done
against confining stress

## Slide 16: Soil strength as two components
[Taylor-Bishop, 1948-50]
Friction
“Strength” = “Friction” + “Interlocking”

## Slide 17: Understanding Terzaghi’s error
Terzaghi model of soil strength
d =
20o
15o
10o
Taylor’s history in ‘light reading’

## Slide 18: Switch from shear-box to triaxial
h = q / p is used instead of… t/sn
D = dev / deq is used instead of… dv/dD
“eta”
“dilatancy”

## Slide 19: Taylor-Bishop strength model in practice
hmax = Mtc – (1-N) Dmin
SAND

## Slide 20: Taylor-Bishop strength model in practice
hmax = Mtc – (1-N) Dmin
CLAY

## Slide 21: What happens before peak strength ?
h = f(D)

## Slide 22: What happens before peak strength ?

## Slide 23: Mobilized friction ratio
Mi = h + D

## Slide 24: Stress-dilatancy at all strains ~1965
h = M – f(D)

## Slide 25
Franklin Falls (NH) 1935
‘sand flow failure'

## Slide 26: Critical state undrained

## Slide 27: 1939: Fort Peck Dam

## Slide 28: Critical state locus: CLAYS ~1955

## Slide 29: Castro: SANDS - Load controlled tests (1969)

## Slide 30: Critical State Locus: SANDS and SILTS ~ 1990
l10
De < ± 0.02

## Slide 31: Void ratio measurement
Large and non-systematic void ratio changes
during saturation

## Slide 32: Measuring void ratio accurately: e = Gs w
Sladen & Handford (1987)
Sladen & Hanford

## Slide 33: Cross-lab trial (freezing method)
Dec = ± 0.02
Seven laboratories
BGC
Golder-Perth Golder-YVR
KCB
TriLabs
U Porto
UWA

## Slide 34: THE QUESTION: In the Taylor-Bishop strength concept...
hmax = Mtc – (1-N) Dmin
Why does a particular value
of Dmin develop ?

## Slide 35
Franklin Falls (NH) 1935
Large Displacement

## Slide 36: Casagrande’s results as math
e
ln(p)
y
y 0 as eg
Casagrande…
First-order rate equation
Notes: Substitute for pc in 1-eta/M = ln(p/pc)

## Slide 37: Limiting dilatancy: A little math (sorry)..
Axiom 2: y 0 as eq ∞ dy = - C y deq
Dmin= C y
Derivation is Appendix A of Course Notes
Concurrent, not initial, value

## Slide 38: And the measured behaviour is: Dmin = C y
Dmin
C

## Slide 39: More soils: Dmin = C y
C

## Slide 40: Strength: hmax = M - (1-N) C y
Effect of fines: Dr does not work
Initial

## Slide 41: How state parameter operates
Stress-dilatancy controlled by dissipation of plastic work
Soil state controls how much dilatancy can develop
SAME SOIL PROPERTIES

## Slide 42: SUMMARY
Soil behaviour is particulate and captured using a few soil properties
    Stress-dilatancy: M, N
    Critical state: G, l10
    State-dilatancy: C
No constitutive model as such involved
Properties do not belong to anybody: just plot data the right way
Developed over about 100 years
Triaxial compression is the reference test to determine soil properties
  Need both drained and undrained
  Need both loose and dense tests

## Slide 43: TUTORIAL 1: Determine properties of a sand
Go to folder Templates for Exercises in the downloaded files
  Beaufort Sea construction sand
  Laboratory testing report as pdf file (note this covers several soils)
  Triaxial data imported to NorTxl2(r11)_Nerlerk_270_(blank).xls
  ‘Enable Macros’ when opening !
YOU …
  Determine: G, l10, M, N, C
      Table with values and possible precision
  Provide plots substantiating your assessment
      Paste into Word as ‘enhanced metafiles’ from xls

## Slide 44: Plots needed (soil property plots)

## Slide 45: Nerlerk Data “Summary & Properties”
1: Summarizes best fits to data
2: Automates calcs in the xls
=‘Test3’!F18

## Slide 46: Step 1: Estimate CSL
Each triaxial test is on its own tabbed sheet
  Review data and assess key values
  Key values transferred to ‘summary’ worksheet
  Work through all undrained tests first
  No loose drained tests in this data
Properties by computing and plotting trend lines
  Adjust G, l10 to get nice fit through critical state
  Investigate the limits of combinations that are plausible

## Slide 47: Nerlerk Data “Soil Property Plots”

## Slide 48: Show engineering judgment adjacent to data

## Slide 49: Now you estimate G and l

## Slide 50: Check the CID data before using.....
Test 3

## Slide 51: Step 2: Get stress-dilatancy properties
Need numerical differentiation to fill this column

## Slide 52: Numerical differentiation (finite difference)
y
x
1
3
2
Dy/Dx at 2 ?
= (y3 – y2) / (x3 – x2)
= (y3 – y1) / (x3 – x1)
= (y2 – y1) / (x2 – x1)
Forward difference
Central difference
Backward difference

## Slide 53: Step 2: Get stress-dilatancy properties
Need numerical differentiation to fill this column

## Slide 54: Step 2: Now you calculate D for Test 3
Numerically differentiate to fill this column

## Slide 55: Why inspect measured data to pick hmax, Dmin
Test 5

## Slide 56: Step 2: Get stress-dilatancy properties

## Slide 57: Determine Mtc, Ntc
From top line of “data review”
use cell references
Dense Drained Tests
“Summary & Properties” sheet
Line 14

## Slide 58: Determining Mtc and Ntc
“Soil Property Plots” sheet
1-N
Mtc
1

## Slide 59: “Summary & Properties”
These cells reference Dmin, hmax and y in the individual tests

## Slide 60: Step 3: Get state-dilatancy properties
For automatic updating as CSL is refined, Cell M14 MUST be a column L cell reference
– NOT just the value

## Slide 61: State dilatancy – C
“Soil Property Plots” sheet
C
(0.0, 0.0)
1

## Slide 62: Inspecting measured data to pick hmax, Dmin, y
Test 5

## Slide 63: Now you estimate M, N and C

## Slide 64: Job done !

## Slide 65: What about clays and silts
Silts
  Same as sand using reconstituted samples
  Drained and undrained loose tests
      M is easy; plot stress-dilatancy of loose drained test for N
      Very difficult to make dense samples with present lab procedures, so need to model a set of test data to get best-estimate of C
Clays
  Remoulded samples to get CSL rare
  Tend to rely on isotropic consolidation or oedometers
      Assume CSL similar slope to NCL
  Consolidated undrained tests
      Be very careful of void ratio change from insitu to as-tested
      Model measured behaviour

## Slide 66: Important aspects of laboratory testing…
Data archiving
Your role !

## Slide 67: Data archiving
You are responsible for proper archiving !
    And keep a copy in your own files…
Many labs submit the lab worksheet as the raw data
    20 MB ? Badly documented ?
    Lab calcs should stay in the lab
Dawn & Mike’s rules: Simple but thorough.
    Use ~3000 points to 20% strain
    Report QA’d: t, s1, s3, e1, ev, e as text file easy import into any software
    Have “header” with details of test including area correction used
    Photo showing deformed shape at end of test
    Add note confirming freezing method for void ratio
    Add note about sample preparation

## Slide 68: Your role
You are the engineer !
Make sure properties are reasonably well defined
  Enough tests ?
  Self-consistent trends ?
  Put the entire QA’d data in a single xls ...Nerlerk.xls
  Model to confirm properties
Write-up properly
  Lab data sheets as appendix ?
    Commonly done, but lots of paper and not much insight
    Might be best left in project files
  Better to have your assessment of properties with summary plots