## Slide 1: 7. Cone Penetration Test - Methodology
Dr. Dawn Shuttle, PEng
Mike Jefferies, PEng
March, 2018

## Slide 2: Overview of Module
What is the CPT, field procedures: getting the data
Assessing the soil types you are dealing with: stratigraphy
Soil state/strength
    Total stress method
    Effective stress method drained
    Effective stress method ‘universal’
    Effective stress method undrained

## Slide 3: The electronic CPTu
fs
u2
qc
Internal electronics with temperature compensation, A-to-D, transmission
Measure inclination, temperature

## Slide 4: Repeatability
About 0.5% of full scale for qc, uc (eg  0.1 MPa)
Friction sleeve worse depending on
    if subtraction cone
    or, independent fs
    your cleaning sleeve

## Slide 5: STEP 1: Select your CPT
Size: 10 cm2 or 15 cm2
Type: ‘subtraction’ or ‘compression’
qc = f()
fs = f()
qc = f()
fs = f() - f()

## Slide 6: Transducer non-linearity and hysteresis
Tip  2% of FSO
Friction  15%
Pore pressure  2%
20 MPa
50 MPa
100 MPa
“Class 1” cones often not good enough for tailings (soft clays)

## Slide 7: A practical issue for CPT: Damage
What you put in the ground you do not always get back…
    Rods can snap if inclination gets too great
    Rods can snap if hard layer encountered with soft ground above
Gravel
Pre-boring through bad ground to get started

## Slide 8: Standards
ASTM D5778 (2012) 
International Reference Standard (in ASTM)
But no standard on data transfer format

## Slide 9: Your choices
A piezocone !
Compression cone of the smallest capacity you can use
    Take a robust cone to first check the ground
Look for 0.5% accuracy cones if in soft ground
At least 14-bit AtoD
A scan rate of 1 Hz
Don’t depend on ASTM or EuroNorm standards
    They are for routine civil engineering, not soft ground

## Slide 10: STEP 2: Setting up the investigation
Where do you expect the weaker ground, what do you know about the depositional environment, what do you know about the geology ?
    You can likely do better than a simple grid-pattern
    And you may be budget constrained
There is more to a CPT campaign that pushing a CPT
    Dissipation tests to define piezometric conditions
    Seismic CPT to establish Gmax profiles
    Some samples (disturbed OK) - MOSTAP

## Slide 11: Cadia: 2017 CPT campaign for upstream raise
Earlier campaigns
2005
2013

## Slide 12: Dissipation tests
If you get piezometric regime wrong, everything else will be wrong
    Measure !
If you have sand layers, then pwp in them can be used as an estimate
    Confirm in each profile with ~2 dissipation tests
Comprehensive dissipation tests in silt/clay strata one-in-four soundings
    Alternatively, devote occasional sounding to dissipation tests
Option of installing piezometers

## Slide 13: Dissipation tests
1 hour

## Slide 14: Underconsolidation

## Slide 15: Perched water table with under-drainage

## Slide 16: STEP 3: Getting ready to push the CPT
Saturation (glycerine)
Ensure clean and open filter stone
Clean friction sleeve ‘O’ rings and gaps
Zeroing, before and after push (< 1% shift)
Vertical

## Slide 17: And keep an eye on where it is going…
Deviation from vertical
    sands seem worse than clays
    may break rods
Want least drillouts
    Efficiency
    Splicing records
Depth correction

## Slide 18: STEP 4: Evaluate ground conditions “interpretation”
STRATIGRAPHIC
    What soil type is where
SAND
    What is their state, friction angle, liquefaction resistance…
    Drained effective-stress methods of evaluation
SILT
    What is their state, friction angle, liquefaction resistance…
    Undrained effective-stress methods of evaluation
    Undrained total-stress methods as supplement
CLAY
    What is the undrained strength su
    Undrained total-stress method
    OCR using undrained effective-stress as supplement

## Slide 19: A testing report is not enough…
GET THE RAW DATA AS DIGITAL FILE
YOU ARE THE ENGINEER

## Slide 20: Data archive: do not rely on corporate procedures
Extensive investigation and special issue of CGJ: 1994
DSR 2010… all original data apparently lost
Head dam of the Columbia River Treaty

## Slide 21: Data archive: be careful of media
600+ sensors, continuously scanned 24/7
~ 20 km of CPT soundings
~ 400+ triaxial tests
~ 200+ SBP tests
Data comprehensively archived by Gulf ~1990
Physically retrieved OK 2010. But….

## Slide 22
Vertical effective stress increases with depth
Soil strength & stiffness increase with stress
CPT response depends on strength and stiffness...
Must remove stress level effects to get to true soil properties/state
Normalizing the data: why ?

## Slide 23: Normalizing as dimensionless numbers...
Rf = fs/qc
sv not sm
uc to be measured at ‘2’ location by standard

## Slide 24: Issues for dimensionless approach
What depth below ground surface did sounding start ?
Where is the water table ?
What are the soil & water unit weights ?
Adding in external knowledge to CPT data

## Slide 25: Soil type identification
Basic use of CPT is to look at soil layering.
Don’t get high qc in clays. Ever.
Relate qc , fs to soil type.
Better framework includes Bq

## Slide 26: Based on case history data...
Q
F
CGJ: Robertson & Campanella (1986)

## Slide 27: First attempt using uc data...
Not as much data behind it as Q-F chart
Sometimes conflicts with Q-F
Bq
Q

## Slide 28: Better approach: use all data at the same time
Q(1- Bq)+1 = (qt-u2)/(sv0-u0)
‘Trust is wonderful, but distrust is better’
    Check with your own case-histories

## Slide 29: Soil classification index: Ic

## Slide 30: Example of stratigraphic evaluation

## Slide 31: Stratigaphy... usually from Bq rather than Ic
Bq

## Slide 32: CPT processing
Import CPT data
Define soil density (approximate) and piezometric conditions
Have a look at the data
    Is what you see consistent with your field notes and QA ?
    What stratigraphy exists ?
    Geologically reasonable ?
Quantitative evaluation of strengths etc

## Slide 33: Load and open CPTplot(r25)_SandExample.xlsm
“enable macros”

## Slide 34: Layout of “CPTplot_*.xls”

## Slide 35: Data import: “CPT data”
CPT data
Dissipation u0
Shear wave vs

## Slide 36: Set unequal area ratio

## Slide 37: Unequal end area correction...
“a” net area ratio
qt = qc + uc (1- a)
Measure

## Slide 38: Define total stress and piezometric conditions

## Slide 39: Program outputs
‘Processed Results’
    All you could ever want for plotting as processed values
    All done in VBA
Three pre-defined output sheets
  ‘Report Fig 1’ …an echo of the data and normalized results plotted by depth
  ‘Report Fig 2’ …the engineering parameters you are interested in (which depend on your choices of method/properties)
  ‘Report Fig 3’ …the soil behaviour type plot (which can be windowed)

## Slide 40: Report Fig 1

## Slide 41: Report Fig 3

## Slide 42: “Interpretation” of CPT data
Need to convert what was measured into what we want
    Do not directly measure s-e
    CPT data must be “interpreted”: Inverse Boundary Value Problem
Detailed fundamental evaluation of CPT beyond current soil mechanics
Methods:
    TOTAL STRESS
        calibrate to a ‘reference’ test (e.g. to su from vane)
    EFFECTIVE STRESS
        calibrate in laboratory using a chamber
        cavity expansion using true soil properties
        ‘universal’ method
    DIRECT TO PERFORMANCE
        relate data to through back-analysis of failures (case-histories)

## Slide 43: Curse of correlations...
Correlations without theoretical basis usually mislead
Can’t get four independent properties from one measurement
Much in situ literature based on unthinking development of correlations

## Slide 44: TOTAL STRESS: CPT evaluation in CLAY
Theory: cavity expansion in Tresca material (1945)
Nk was weak theoretical dependence on G/su
Wider range of Nk encountered in practice

## Slide 45: Where does Nk come from ?
By calibration to a ‘reference’ test
    Triaxial compression (various protocols)
    Vane shear (assumed geometry, possible rate effect corrections)
    Self-bored pressuremeter
CPT is being used to interpolate between the ‘reference’ strengths
BUT there is a pattern with similar values for similar geological conditions

## Slide 46
Soft clays
Very stiff clays
Nk = 11
Nk = 16

## Slide 47: Getting su from SBP: Paddington

## Slide 49: Input of Nkt factor
If an equation is outside its limit of validity at a particular data point, then ‘999’ is output to the Processed Results
Nkt now computed by CPTwidget if undrained
Undrained if:
|Bq|>0.1 or F>1%

## Slide 50: OCR from CPT
Q
Kulhawy & Mayne (1990)
Mesri (2001)
Demers & Leroueil (2002)

## Slide 51: Nearly everything is in VBA

## Slide 52: Open Code…

## Slide 53: Output from VBA routines